| Project: |  |
| --- | --- |
| Location: |  |
| Owner: |  |
| Design Professional in Responsible Charge: |  |

This Statement of Special Inspections is submitted as a condition for permit issuance in accordance with the Special Inspection and Structural Testing requirements of the Building Code.  It includes a schedule of Special Inspection services applicable to this project as well as the name of the Special Inspection Coordinator and the identity of other approved agencies to be retained for conducting these inspections and tests.  This Statement of Special Inspections encompasses all aspects of Structural Tests and Special Inspections as stated in Chapter 17, IBC, as adopted.

The Special Inspection Coordinator shall keep records of all inspections performed and shall furnish inspection reports to the Director of Planning and the Registered Design Professional in Responsible Charge.  Discovered discrepancies shall be brought to the immediate attention of the Contractor for correction.  If such discrepancies are not corrected, the discrepancies shall be brought to the attention of the Director of Planning and the Registered Design Professional in Responsible Charge.  The Special Inspection program does not relieve the Contractor of his or her responsibilities.

Interim reports shall be submitted to the Director of Planning and the Registered Design Professional in Responsible Charge.

A Final Report of Special Inspections documenting completion of all required Special Inspections, testing and correction of any discrepancies noted in the inspections shall be submitted prior to issuance of a Certificate of Use and Occupancy.

| Interim Report Frequency: |  | or per attached schedule. |
| --- | --- | --- |
| Prepared by: |  | Design Professional Seal |
| (type or print name) |  |  |
| Signature | Date |  |  |

| Owner’s Authorization: |  | Director of Planning Acceptance: |
| --- | --- | --- |
| Signature | Date |  | Signature | Date |

Page       of

## Schedule of Inspection and Testing Agencies

This Statement of Special Inspections / Quality Assurance Plan include the following building systems:

Soils and Foundations			   Spray Fire Resistant Material

Cast-in-Place Concrete			   Wood Construction

Precast Concrete				   Exterior Insulation and Finish System

Masonry					   Mechanical & Electrical Systems

Structural Steel				   Architectural Systems

Cold-Formed Steel Framing		   Special Cases

| Special Inspection Agencies | Firm | Address, Telephone, e-mail |
| --- | --- | --- |
| 1. Special Inspection Coordinator |  |  |
| 2. Inspector |  |  |
| 3. Inspector |  |  |
| 4. Testing Agency |  |  |
| 5. Testing Agency |  |  |
| 6. Other |  |  |

Note:  The inspectors and testing agencies shall be engaged by the Owner or the Owner’s Agent, and not by the Contractor or Subcontractor whose work is to be inspected or tested. Any conflict of interest must be disclosed to the Director of Planning, prior to commencing work.

Page       of

Quality Assurance Plan

###### Quality Assurance for Seismic Resistance

| Seismic Design Category |  |
| --- | --- |
| Quality Assurance Plan Required (Y/N) |  |
| Description of seismic force resisting system and designated seismic systems: |

Quality Assurance for Wind Requirements

| Basic Wind Speed (3 second gust) |  |
| --- | --- |
| Wind Exposure Category |  |
| Quality Assurance Plan Required (Y/N) |  |
| Description of wind force resisting system and designated wind resisting components: |

Statement of Responsibility

Each contractor responsible for the construction or fabrication of a system or component designated above must submit a Statement of Responsibility.

| Soils and Foundations |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Shallow Foundations | PE/GE | Inspect soils below footings for adequate bearing capacity and consistency with geotechnical report. Inspect removal of unsuitable material and preparation of subgrade prior to placement of controlled fill |
| 2. Controlled Structural Fill | PE/GE | Perform sieve tests (ASTM D422 & D1140) and modified Proctor tests (ASTM D1557) of each source of fill material. Inspect placement, lift thickness and compaction of controlled fill. Test density of each lift of fill by nuclear methods (ASTM D2922) Verify extent and slope of fill placement. |
| 3. Deep Foundations | PE/GE | Inspect and log pile driving operations. Record pile driving resistance and verify compliance with driving criteria. Inspect piles for damage from driving and plumbness. Verify pile size, length and accessories. Inspect installation of drilled pier foundations. Verify pier diameter, bell diameter, lengths, embedment into bedrock and suitability of end bearing strata. |
| 4. Load Testing |  |  |
| 4. Other: |  |  |

| Cast-in-Place Concrete |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Mix Design | ACI-CCI ICC-RCSI | Review concrete batch tickets and verify compliance with approved mix design. Verify that water added at the site does not exceed that allowed by the mix design. |
| 2. Material Certification |  |  |
| 3. Reinforcement Installation | ACI-CCI ICC-RCSI | Inspect size, spacing, cover, positioning and grade of reinforcing steel. Verify that reinforcing bars are free of form oil or other deleterious materials. Inspect bar laps and mechanical splices. Verify that bars are adequately tied and supported on chairs or bolsters |
| 4. Post-Tensioning Operations | ICC-PCSI | Inspect placement, stressing, grouting and protection of post-tensioning tendons. Verify that tendons are correctly positioned, supported, tied and wrapped. Record tendon elongations. |
| 5. Welding of Reinforcing | AWS-CWI | Visually inspect all reinforcing steel welds. Verify weldability of reinforcing steel. Inspect preheating of steel when required. |
| 6. Anchor Rods |  | Inspect size, positioning and embedment of anchor rods. Inspect concrete placement and consolidation around anchors. |
| 7. Concrete Placement | ACI-CCI ICC-RCSI | Inspect placement of concrete. Verify that concrete conveyance and depositing avoids segregation or contamination. Verify that concrete is properly consolidated. |
| 8. Sampling and Testing of Concrete | ACI-CFTT ACI-STT | Test concrete compressive strength (ASTM C31 & C39), slump (ASTM C143), air-content (ASTM C231 or C173) and temperature (ASTM C1064). |
| 9. Curing and Protection | ACI-CCI ICC-RCSI | Inspect curing, cold weather protection and hot weather protection procedures. |
| 10. Other: |  |  |

| Precast Concrete | Page of |
| --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Plant Certification / Quality Control Procedures Fabricator Exempt | ACI-CCI ICC-RCSI | Review plant operations and quality control procedures. |
| 2. Mix Design | ACI-CCI ICC-RCSI | Inspect concrete batching operations and verify compliance with approved mix design |
| 3. Material Certification |  |  |
| 4. Reinforcement Installation | ACI-CCI ICC-RCSI | Inspect size, spacing, position and grade of reinforcing steel. Verify that reinforcing bars are free of form oil or other deleterious materials. |
| 5. Prestress Operations | ICC-PCSI | Inspect placement, stressing, grouting and protection of prestressing tendons |
| 6. Connections / Embedded Items |  |  |
| 7. Formwork Geometry |  |  |
| 8. Concrete Placement | ACI-CCI ICC-RCSI | Inspect placement of concrete. Verify that concrete conveyance and depositing avoids segregation or contamination. Verify that concrete is properly consolidated. |
| 9. Sampling and Testing of Concrete | ACI-CFTT ACI-STT | Test concrete compressive strength (ASTM C31 & C39), slump (ASTM C143), air-content (ASTM C231 or C173) and temperature (ASTM C1064). |
| 10. Curing and Protection | ACI-CCI ICC-RCSI | Inspect curing, cold weather protection and hot weather protection procedures. |
| 11. Erected Precast Elements | PE/SE | Inspect erection of precast concrete including member configuration, connections, welding and grouting. |
| 12. Other: |  |  |

| Masonry | Required Inspection Level: 1 2 | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Material Certification |  |  |
| 2. Mixing of Mortar and Grout | ICC-SMSI | Inspect proportioning, mixing and re-tempering of mortar and grout. |
| 3. Installation of Masonry | ICC-SMSI | Inspect size, layout, bonding and placement of masonry units. |
| 4. Mortar Joints | ICC-SMSI | Inspect construction of mortar joints including tooling and filling of head joints. |
| 5. Reinforcement Installation | ICC-SMSI AWS-CWI | Inspect placement, positioning and lapping of reinforcing steel. Inspect welding of reinforcing steel. |
| 6. Pre-stressed Masonry | ICC-SMSI | Inspect placement, anchorage and stressing of pre-stressing bars. |
| 7. Grouting Operations | ICC-SMSI | Inspect placement and consolidation of grout. Inspect masonry clean-outs for high-lift grouting. |
| 7. Weather Protection | ICC-SMSI | Inspect hot weather protection procedures. Verify that wall cavities are protected against precipitation. |
| 9. Evaluation of Masonry Strength | ICC-SMSI | Test compressive strength of mortar and grout cube samples (ASTM C780). Test compressive strength of masonry prisms (ASTM C1314). |
| 10. Anchors and Ties | ICC-SMSI | Inspect size, location, spacing and embedment of dowels, anchors and ties. |
| 11. Other: |  |  |

| Structural Steel | Page of |
| --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Fabricator Certification/ Quality Control Procedures Fabricator Exempt | AWS/AISC-SSI ICC-SWSI | Review shop fabrication and quality control procedures. |
| 2. Material Certification | AWS/AISC-SSI ICC-SWSI | Review certified mill test reports and identification markings on wide-flange shapes, high-strength bolts, nuts and welding electrodes |
| 3. Open Web Steel Joists |  | Inspect installation, field welding and bridging of joists. |
| 4. Bolting | AWS/AISC-SSI ICC-SWSI | Inspect installation and tightening of high-strength bolts. Verify that splines have separated from tension control bolts. Verify proper tightening sequence. Continuous inspection of bolts in slip-critical connections. |
| 5. Welding | AWS-CWI ASNT | Visually inspect all welds. Inspect pre-heat, post-heat and surface preparation between passes. Verify size and length of fillet welds. Ultrasonic testing of all full-penetration welds. |
| 6. Shear Connectors | AWS/AISC-SSI ICC-SWSI | Inspect size, number, positioning and welding of shear connectors. Inspect suds for full 360 degree flash. Ring test all shear connectors with a 3 lb hammer. Bend test all questionable studs to 15 degrees. |
| 7. Structural Details | PE/SE | Inspect steel frame for compliance with structural drawings, including bracing, member configuration and connection details. |
| 8. Metal Deck | AWS-CWI | Inspect welding and side-lap fastening of metal roof and floor deck. |
| 9. Other: |  |  |

| Cold-Formed Steel Framing |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Member Sizes |  |  |
| 2. Material Thickness |  |  |
| 3. Material Properties |  |  |
| 4. Mechanical Connections |  |  |
| 5. Welding |  |  |
| 6. Framing Details |  |  |
| 7. Trusses |  |  |
| 8. Permanent Truss Bracing |  |  |
| 9. Other: |  |  |

| Spray-Applied Fire Resistant Material |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Material Specifications |  |  |
| 2. Laboratory Tested Fire Resistance Design | ICC-SFSI | Review UL fire resistive design for each rated beam, column, or assembly. |
| 3. Schedule of Thickness | ICC-SFSI | Review approved thickness schedule. |
| 4. Surface Preparation | ICC-SFSI | Inspect surface preparation of steel prior to application of fireproofing |
| 5. Application | ICC-SFSI | Inspect application of fireproofing. |
| 6. Curing and Ambient Condition | ICC-SFSI | Verify ambient air temperature and ventilation is suitable for application and curing of fireproofing. |
| 7. Thickness | ICC-SFSI | Test thickness of fireproofing (ASTM E605). Perform a set of thickness measurements for every 1,000 SF of floor and roof assemblies and on not less than 25% of rated beams and columns. |
| 8. Density | ICC-SFSI | Test the density of fireproofing material (ASTM E605). |
| 9. Bond Strength | ICC-SFSI | Test the cohesive/adhesive bond strength of fireproofing ASTM E736). Perform not less than one test for each 10,000 SF. |
| 10. Other: |  |  |

| Wood Construction |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Fabricator Certification/ Quality Control Procedures Fabricator Exempt |  | Inspect shop fabrication and quality control procedures for wood truss plant. |
| 2. Material Grading |  |  |
| 3. Connections |  |  |
| 4. Framing and Details |  |  |
| 5. Diaphragms and Shear walls |  | Inspect size, configuration, blocking and fastening of shear walls and diaphragms. Verify panel grade and thickness. |
| 6. Prefabricated Wood Trusses |  | Inspect the fabrication of wood trusses. |
| 7. Permanent Truss Bracing |  |  |
| 8. Other: |  |  |

| Exterior Insulation & Finish Systems (EIFS) |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Material Submittals |  |  |
| 2. Condition of Substrate |  |  |
| 3. Application of Foam Plastic Board |  |  |
| 4. Application of Coatings |  |  |
| 5. Application of Mesh |  |  |
| 6. Ambient Condition and Curing |  |  |
| 7. Flashing and Joint Details |  |  |
| 8. Sealants/Caulks |  |  |
| 9. Other: |  |  |

| Mechanical & Electrical Systems |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Smoke Control |  |  |
| 2. Mechanical, HVAC & Piping |  |  |
| 3. Electrical System |  |  |
| 4. Other: Medical Gas |  |  |

| Architectural Systems |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |
| 1. Wall Panels & Veneers |  |  |
| 2. Suspended Ceilings |  |  |
| 3. Access Floors |  |  |
| 4. Other: |  |  |

| Special Cases |  | Page of |
| --- | --- | --- |

Statement of Special Inspection must state either periodic or continuous inspection and shall be specific to each project.

| Item | Agency # (Qualif.) | Scope |
| --- | --- | --- |

SPECIAL INSPECTION DAILY REPORT

Permit No.: 	  Date:

Project Name/Address:

Inspection type(s) coverage:

(  Continuous 	(  Periodic

Inspection time: Beginning:__________	Ending:__________

Describe inspections performed, including locations:

Tests performed:

New Items needing correction:

Corrected items from previous reports:

Item corrections remaining incomplete:

Changes to approved plans authorized by Registered Design Professional in Responsible Charge:

1 of 2

Comments:

To the best of my knowledge, the work inspected was in accordance with the Department of Planning approved plans, specifications and applicable workmanship provisions of the IBC except as noted above.

Signed: _______________________

Inspection Agency*: _____________________________

Full Name (print):

Cc: Project Owner

SPECIAL INSPECTION WEEKLY REPORT

Permit No.:  	  Date:

Project Name/Address:

Total inspection time each day:

| Date |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Hours |  |  |  |  |  |  |  |
| Inspection Type |  |  |  |  |  |  |  |
| Frequency (P or C) |  |  |  |  |  |  |  |
| Location |  |  |  |  |  |  |  |

P – Periodic inspection

C – Continuous inspection

Describe inspections made, including locations:

Tests   performed:

New Items needing correction:

Corrected items from previous reports:

Item corrections remaining incomplete:

Changes to approved plans authorized by Registered Design Professional in Responsible Charge:

Comments:

To the best of my knowledge, the work inspected was in accordance with the approved plans, specifications and applicable workmanship provisions of the Cayman Islands Building Code except as noted above.

Full Name (print): _____________________________________

Signed: ___________________________

Special Inspector

SPECIAL INSPECTION FINAL REPORT

Project Name/Address:

Permit No.: 	  Date:

Attention:

In accordance with Chapter 17 of the Cayman Islands Building Code, special inspection has been provided   for   the   following   items:

I certify that I performed special inspection on the following portions of the work at the above address that required continuous inspections, and for which I was employed.

Based upon inspections performed and my substantiating reports, it is my professional judgment that, to the best of my knowledge, the inspected work was performed in accordance with the approved plans, specifications and applicable workmanship provisions of the Cayman Islands Building Code.

Full Name (print):

ID / Certificate Number:

Signed: ________________________

Inspection Agency*:

STRUCTURAL OBSERVER DISCREPANCY NOTICE

Permit #:  	  Date:

Name/Address:

Structural Observation Type/Coverage:

Notice delivered to:

 Contractor              Engineer/Architect             Department of Planning

 Special Inspector    Owner

Signature:

Full Name (print):

Company: _________________________